# Fence Specifications for Kentucky Mesonet Sites

Site host agrees to furnish all materials, labor, equipment, supplies, etc to complete the following scope of work.  Furnish and install 160’ of 6’ high of 9 gauge chain link fence with 3 strands of barbed wire on top with 2” weave fabric and all posts set in concrete.  There will be one 12’ double drive gate.

Overall Length:	160’

Overall Height: 	6’ + 3

Drive Gate	12’0”

Mesh	2”

CHAIN LINK

Wire Gauge	9

Diameter Terminal Post	3”+4” Std 40

Diameter Line Post	2” Std 40

Diameter Post Rail	1 5/8” Std 40

Diameter Gate Frame	1 5/8” Std 40

Line Post Spacing	Approx 10’

Barb Up	Yes

SPECIFICATIONS

Top Rail of Fence will Parallel Ground

Fence Line will be Cleared of Obstructions

All Posts will be Set in Concrete

# Text boxes

Copyright © 2007, Kentucky Climate Center, Western Kentucky University